## Slide 1
Wind Turbine Locations
Digital Elevation Model
Compute Relative Viewsheds
Blade End
Hub
Rotor Sweep
Create for each location separately
Reclassify Relative Viewsheds
Merge Relative Viewsheds
Store maximum in each pixel and calculate for each wind turbine
(Palmer 2022)
Blade End [255:10]
Hub [255:20]
Rotor Sweep [255:30]
0 – No Visibility
255 – Complete Visibility
Compute Multi Ring Buffer
Create for each location separately
Rasterize Multi Ring Buffer
Immediate: 0 – 0.8 KM
Foreground: 0.8 – 3.2 KM
Near-Midground: 3.2 – 8 KM
Far-Midground: 8 – 16.1 KM
Background: 16.1 – 32.2 KM
Immediate: 1
Foreground: 2
Near-Midground: 3
Far-Midground: 4
Background: 5
Merge Rasters
Visual Exposure Raster
Distance Zone Raster
Raster Sum (Visual Exposure, Distance Zone)
Reclassify as per Table 3
Reclassify as per Table 4
(Palmer 2022)
(Palmer 2022)
Visual Prominence Raster
Meaningful Visibility Raster
Cumulative Visual Prominence
Cumulative Meaningful Visibility
Raster Division
Mean Visual Prominence Raster
Raster Value Extraction
Final Step
Turbine Visual Prominence Bubble Plot
GIS Workflow of Visual Impact Assessment (VIA)